IMPORTANT:	Before attempting installation, please read these instructions fully

WARNING: 	DO NOT use the PRO/STREET Nodular Iron Crankshaft Damper in Any Racing Application.

NOTE: For racing, utilise our ‘ALL STEEL’ PRO/RACER SFI Spec. 18.1 approved Dampers.

NOTE: The PRO/STREET Crankshaft Damper has a precision machined inner bore which requires special attention prior to fitting. It is also important to note that your PRO/STREET Damper is supplied "IN BALANCE" condition, therefore, if any balancing operations are to be carried out on the engine, weight must be added or removed from the crankshaft only.

Important: DO NOT drill any hole in your PRO/STREET Damper when Dynamically Balancing your Engine.

1.	Engine must be completely cold.

2.  	Remove original Damper, using a Damper puller or removal tool.

3. 	Inspect crankshaft snout to ensure there are no burrs or rust, if required polish with very fine emery paper or steel wool, wash clean.

4. 	Examine key, should the key be damaged or loose in the key-way groove of the crankshaft, install a new key.

5. 	Replace the front timing cover oil seal.

6.  	The PRO/STREET Crankshaft Damper can be installed using a Damper Installation Tool. However, you can make installation much easier by placing Damper in a pre-heated oven at the lowest temperature (max. 250oF or 120oC) for 15 minutes. This process will expand the hub of the Damper.

7. 	If you are NOT using a Damper Installation Tool, it is ESSENTIAL that the Damper be pre-heated as outlined in step 6. above, to expand the hub. All subsequent steps will need to be followed carefully.

8.  	Smear crank snout and the timing case oil seal with clean oil.

9. 	If you are not using a Damper Installation Tool, remove Damper from oven, using insulated, heat proof gloves. Smear bore of Damper with oil.

10. 	Immediately locate Damper on to the crankshaft and rotate until the hub locates in the key-way.

IMPORTANT - DO NOT ALLOW DAMPER TO COOL.

11.	If using a Damper Installation Tool, install the Damper following the instructions supplied with your installation tool and ignore step 12.

12.	If you are not using an Installation Tool, quickly, utilizing a block of aluminum to protect the machined face, drive the Damper on the crankshaft.

13.	Promptly reinstall the Damper retaining bolt and washer and tension to 100 lb/ft torque.

NOTE:   Use LOCTITE to secure the crankshaft and pulley bolts.

14. 	Check that the pulley alignment is correct.

15. 	Recheck for adequate clearance of all components before re-starting engine.

Should you have any issues fitting your PRO/STREET Damper, please contact PRO/STREET Tech-line.

USA: 	PRO/RACE Tech-line		Tel: 734 740 0922

USA: 	PRO/RACE Tech-line, CA:	                Tel: 1 800 977 0767		Fax: 1 800 803 0087

Australia:	PRO/RACE Tech-line		Tel: +61 3 9584 3522		Fax: +61 3 9584 5194

Email: 	tech@pro-race.com		Website: www.pro-race.com

17Sept2018